## Slide 1
SFH881CA402 Analysis Report
Wisol Hanoi Co.,Ltd
Notes: 1

## Slide 2
Contents
Team Member
Problem Description
1
2
Containment Action
Root Cause Analysis
3
4
Corrective Action
Verification of Correction Actions
5
6
Preventive Action
Approval
7
8
Notes: 2

## Slide 3
Origin information |  |  | 
Producing Area | Part | Code Number | Contact Person
WHC | SFH881CA402 | - | WHC QC Jo Deok rae
T/F TEAM |  |  | 
Team | Members | Details | Remark
制造 | Park Jae wan Principle Manager | Group Leader | -
制造 | Moon Hyung seok Manager | 驻在员 | 
制造 | Phan van due | Part leader | 
品质 | Jo Deo krae Senior Manager | Group Leader | 
品质 | Nguyen Thi Mai Assistant Manager | Part leader | 
WTC 品质 | 金彪 科长 | CS 担当 | 
Team Member
1
Notes: 3

## Slide 4
■ Received History
Item | Contents
Received Date | 2022.01.07
Site | vivo
P/N | B5 SFH881CA402
Defect Phenomenon | B5/BC0/GSM850 DRX校准失败
Defect Qty | 1 EA / 40 EA（新项目前期）
Factory | WHC
Marking / Reel No | Rmlo E / CNM073FFD00104
Received Qty. | 1ea
Problem Description
2
Notes: 4

## Slide 5
SPL #1
■ RF Measure
1) User Waveform _ vivo
Problem Description
2

## Slide 6
■ Visual Inspection
1) No Problem
Problem Description
2
 | SPL #1
Top | 
Bottom | 

## Slide 7
■ X-RAY:
1) No Problem
 | SPL #1
Top | 
Problem Description
2

## Slide 8
SPL #1
■ RF Measure
1) Waveform Fail
Problem Description
2

## Slide 9
■ C Value 分析
1511 | 1-2 | 4-5 | Result
Min | 2.5 | 3.6 | -
Max | 3.0 | 4.1 | -
#1 | 3.09 | 4.95 | Fail
2) C值 测量结果
1) Bottom Pin Map
Unit：pF
Problem Description
2

## Slide 10
■ De-cap 分析
1) 分析失败（De-cap时，Chip破损）
- Bump 焊接状态良好
Problem Description
2
Chip
Ceramic PKG

## Slide 11
No | Items | Result
1 | Phenomenon analysis | No Problem
2 | X-Ray | No Problem
3 | Frequency analysis | RF Fail
4 | C Value analysis | Fail
5 | Decap analysis | 分析失败
■ Analysis Summary
Problem Description
2
Notes: 11

## Slide 12
Containment Action
3
■ Affect LOT: 按照Marking 基准 280K，其中vivo 210K
- 邀请临时隔离 210K，Lot List 如下；
- 另外 CNM073FFD00104（VOC Lot）残量 Reel 发送给天津Retest 及继续分析
Lot ID | Reel ID | Rework | Q'Ty | Marking No | Customer Name | Ship Reel | Remark
CNM073FFD00100 | CNM045FF800107 |  | 10,000 | RmIo E | UASCENT | RHFFP0000Z | 
 | CNM073FFD00101 |  | 10,000 |  | UASCENT | RHFFP0000X | 
 | CNM073FFD00102 |  | 10,000 |  | UASCENT | RHFFP0000W | 
 | CNM073FFD00103 |  | 10,000 |  | UASCENT | RHFFP0000V | 
 | CNM073FFD00104 |  | 10,000 |  | UASCENT | RHFFP00010 | 
 | CNM073FFD00105 |  | 10,000 |  | UASCENT | RHFFP0000Y | 
 | CNM073FFD00106 |  | 10,000 |  | UASCENT | RHFFP0003D | 
CNM073FFD00200 | CNM045FFC00007 |  | 10,000 | RmIo E | SUNNY | RHFFT0003H | 
 | CNM073FFD00201 |  | 10,000 |  | SUNNY | RHFFT0003F | 
 | CNM073FFD00202 |  | 10,000 |  | SUNNY | RHFFT0003E | 
 | CNM073FFD00203 |  | 10,000 |  | SUNNY | RHFFT0003J | 
 | CNM073FFD00204 |  | 10,000 |  | SUNNY | RHFFT0003G | 
 | CNM073FFD00205 |  | 10,000 |  | SUNNY | RHFFT0003I | 
 | CNM073FFD00206 |  | 10,000 |  | SUNNY | RHFFT0002Y | 
CNM045FFE00000 | CNM045FFC00107 |  | 10,000 | RmIo E | UASCENT | RHFFP00014 | 
 | CNM045FFE00001 |  | 10,000 |  | UASCENT | RHFFP00013 | 
 | CNM045FFE00002 |  | 10,000 |  | UASCENT | RHFFP00015 | 
 | CNM045FFE00003 |  | 10,000 |  | UASCENT | RHFFP00016 | 
 | CNM045FFE00004 |  | 10,000 |  | UASCENT | RHFFP00011 | 
 | CNM045FFE00005 |  | 10,000 |  | UASCENT | RHFFP00012 | 
 | CNM045FFE00006 |  | 10,000 |  | UASCENT | RHFFP00039 | 
CNM045FFE00100 | CNM073FFM00007 |  | 10,000 | RmIo E | UASCENT | RHFFQ000CE | 
 | CNM045FFE00101 |  | 10,000 |  | UASCENT | RHFFQ000CH | 
 | CNM045FFE00102 |  | 10,000 |  | UASCENT | RHFFQ000CG | 
 | CNM045FFE00103 |  | 10,000 |  | UASCENT | RHFFQ000CI | 
 | CNM045FFE00104 |  | 10,000 |  | UASCENT | RHFFQ000CD | 
 | CNM045FFE00105 |  | 10,000 |  | UASCENT | RHFFQ000CF | 
 | CNM045FFE00106 | CTM038FFQ00001 | 10,000 |  | UASCENT | RHFLA0008A | :COVER TAPE DEFECT: :包装盖带不良;

## Slide 13
Containment Action
3
■ Affect LOT Yield, O/S Defect rate Status
Chart: Affect LOT Yield, Defect Rate
| CNM073FFD00100 | CNM073FFD00200 | CNM045FFE00000 | CNM045FFE00100
Yield [%] | 0.96571 | 0.98232 | 0.97475 | 0.95596
P05D [%] | 0.00068646 | 0.0006261 | 0.0005463 | 0.00019804
P10D [%] | 0.003417 | 0.0030694 | 0.0045373 | 0.0043568
Issue Lot
※ Keep Sample 분석 진행 시 VOC 불량 유형과 동일 유형 파형 없음

## Slide 14
Thank you !